##### Initial setup
- Setup VLANs - Interfaces → Devices → VLAN
  - Management 99
  - WiFi 20
  - WiFi guest 22
- Assign interfaces - Interfaces → Assignments → choose an interface
  - Parent : LAN
  - IPv4 config type : Static IPv4, IPv4 address 192.168.xx.1 / 24
- Navigate to System → Settings → Administration and change the TCP port field to something other than 80 or 443. Then, also check the HTTP Redirect field to disable web GUI redirect rule.
- Services:
  - ISC DHCPv4 → Interface → Enable DHCP server, specify range (x.x.x.100 to 199)
##### Backup
System → Configuration → Backups